## Slide 1: Adaptive Waste Collection Routing
Omar ALShaye
Emilio Mantilla
Greg Bernstein
Notes: Omar

## Slide 2: Business Case
Notes: Omar

## Slide 3: Problem Definition:
Solid waste collection follows static view: Waste is collected from every collection point
Opportunity in understanding fill status of collection points and scheduling accordingly in an iterative approach
Goal: reduce collection trucks weekly travel
Notes: Omar

## Slide 4: Modeling
Notes: Omar

## Slide 5: Our Problem: VRPPD Instance of TSP
Vehicle Routing Problem with Pickup and Delivery (VRPPD): A number of goods need to be moved from certain pickup locations to other delivery locations
The goal is to find optimal routes for a fleet of vehicles to visit the pickup and drop-off locations
Notes: Omar

## Slide 6: Model
Objective Function: Minimize Travel Distance:
Constraint I: exactly one arc enters each vertex associated with a customer
Constraint II: exactly one arc leaves each vertex associated with a customer
Customer 1
Customer 2
Notes: Omar:
X is distance between previous customer I and next customer j
K = number of vehicles

## Slide 7: Model continued.
Constraint III and IV: number of vehicles leaving the depot is the same as the number entering
Constraint V: capacity cut constraints, imposing that the routes must be connected and that the demand on each route must not exceed the vehicle capacity
Constraint VI: Integrality Constraints:
Notes: Omar

## Slide 8: NP Hardness
VRP is NP hard combinatorial optimization problem that can be exactly solved only for small instances of the problem.
NP-hard problems are problems for which there is no known polynomial algorithm, so that the time to find a solution grows exponentially with problem size.
TSP has to visit 1 to n. Trivial Solution O(n!) permutations:
For problem with 500 points, there are 500! permutations:
  1220136825991110068701238785423046926253574342803192842192413588385845373153881997605496447502203281863013616477148203584163378722078177200480785205159329285477907571939330603772960859086270429174547882424912726344305670173270769461062802310452644218878789465754777149863494367781037644274033827365397471386477878495438489595537537990423241061271326984327745715546309977202781014561081188373709531016356324432987029563896628911658974769572087926928871281780070265174507768410719624390394322536422605234945850129918571501248706961568141625359056693423813008856249246891564126775654481886506593847951775360894005745238940335798476363944905313062323749066445048824665075946735862074637925184200459369692981022263971952597190945217823331756934581508552332820762820023402626907898342451712006207714640979456116127629145951237229913340169552363850942885592018727433795173014586357570828355780158735432768888680120399882384702151467605445407663535984174430480128938313896881639487469658817504506926365338175055478128640000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000
Notes: Omar
In computational complexity theory, P, also known as PTIME or DTIME(nO(1)), is a fundamental complexity class. It contains all decision problems that can be solved by a deterministic Turing machine using a polynomial amount of computation time, or polynomial time.

## Slide 9: Heuristic Approach
This Means we need a
“A heuristic technique (/hjʊəˈrɪstɪk/; Ancient Greek: εὑρίσκω, "find" or "discover"), often called simply a heuristic, is any approach to problem solving or self-discovery that employs a practical method, not guaranteed to be optimal, perfect, logical, or rational, but instead sufficient for reaching an immediate goal. ”
Notes: Omar

## Slide 10
1
2
3
4
5
6
2
4
2
1
3
4
2
3
2
1
2
3
5
6
Kruskal’s Minimum Spanning Tree Algorithm:
Given a connected and undirected graph, find the min spanning tree of that graph is a subgraph that is a tree and connects all the vertices together
4
Rules:
1. At each node, sort all the edges in non-decreasing order of their weight.
2. Pick the smallest edge. Check if it forms a cycle with the spanning tree formed so far. If cycle is not formed, include this edge. Else, discard it.
3. Repeat step#2 until there are (V-1) edges in the spanning tree.
Problem:
Low Performing Greedy Model
Does not form route (only min spanning tree)
Notes: Greg Interactive

## Slide 11
Dijkstra’s / Clarke Wright Savings
Algorithm
1
2
3
4
5
6
2
4
2
1
3
4
2
3
2
d(2) = 
pred(2) =
LIST = { 1,
d(1) = 0
pred(1) = 0
d(4) = 
pred(4) =
d(3) = 
pred(3) =
d(5) = 
pred(5) =
d(6) = 
pred(6) =
\ 2, 3,
\ 2
1
\ 4
1
\ 6
2
\ 4
2
\ 4, 5,
\
\ 6
5
\ 6}
\
\
\ 3
\ 2
Initialize the distances and LIST.
Find the node i on LIST with minimum distance.
Scan the arcs out of i, and update d( ), pred( ), and LIST
1
Find the node i on LIST with minimum distance.
2
Scan the arcs out of i, and update d( ), pred( ), and LIST
Find the node i on LIST with minimum distance.
3
Scan the arcs out of i, and update d( ), pred( ), and LIST
Find the node i on LIST with minimum distance.
5
Scan the arcs out of i, and update d( ), pred( ), and LIST
Find the node i on LIST with minimum distance.
4
Scan the arcs out of i, and update d( ), pred( ), and LIST
Find the node i on LIST with minimum distance.
6
The End
Notes: Greg Interactive

## Slide 12: Simulating Inputs
Notes: Emilio

## Slide 13: Assumptions
Our goal is to review and compare distance travelled, amount of trash collected, and other metrics for different required levels of trash collection.
We assume that there is one garbage truck and that it is required to start and end it’s journey from a central depot. The truck is required to visit every home that has at least X% of filled trash capacity once and only once.
We assume that there are no storage limitations within the truck. That is, a truck could collect trash from every household in the city if each household was at 100% capacity.
We assume that trash is collected once a week, and we monitor the progress of collection over a 5 week period.
Notes: Emilio

## Slide 14: Geographical Inputs
We use Portland, ME as a target city, where garbage collectors visit approximately 900 homes per day. For computational purposes, we simulate 500 homes.
We placed a trash depot at central longitude and latitude coordinates of Portland: 43.4°N and 70.16°W.
We created maximum and minimum longitudinal values based on the central coordinates and Portland have a square mileage area = 21.31. Conversion factors of 1 degree lat = 69 miles and 1 degree long = 53 miles were used.
500 homes were uniformly randomly simulated within this square area with all possible values of longitude and latitude being equally likely.
The Euclidean distance between each home was calculated
Notes: Emilio

## Slide 15: Distance Matrix
501x501 triangular matrix of distances between houses
Notes: Emilio

## Slide 16: Input Simulation
The amount of trash generated by each household in week 1 was simulated as a value between 0 and 1, representing percentage of capacity full.
Trash generated was simulated according to the following distribution:
  75% probability of being between 20-80% full. Uniform in this range
  10% prob of being 0-20% full. Uniform in this range.
  15% prob of being 80-100% full. Uniform in this range.
Trash amounts in following weeks were simulated as being within a 5% range of the week 1 amount. Uniform in this range.
Notes: Emilio

## Slide 17: Solvers
Notes: Greg

## Slide 18: Solvers
Gregs fnction / lehigh solver
Notes: Greg

## Slide 19: Results
Notes: Greg

## Slide 20: Algorithm Comparison
Chart: Distance Travelled (Miles)
| Week I | Week II | Week III | Week IV | Week V
Full Collection CW | 81.4902 | 81.4902 | 81.4902 | 81.4902 | 81.4902
>45% Collection CW | 61.1227 | 73.1352 | 63.7817 | 73.0603 | 63.1661
Full Collection Min | 91.6437 | 91.6437 | 91.6437 | 91.6437 | 91.6437
>45% Collection Min | 68.2063 | 84.1403 | 73.573 | 86.024 | 74.9083
Total
407.45
334.25
458.22
386.85
13.6% Decrease in Miles Travelled Over 5 Weeks by using Clark Wright algorithm
Min W1 | CW W1 | CW W3
1 | 1 | 1
137 | 72 | 137
106 | 413 | 106
397 | 408 | 273
495 | 377 | 30
Routes
Notes: Greg: Add route comparison in addition to distance comparison

## Slide 21: Waste Collection Composite Index
Notes: Omar

## Slide 22: Minimum Distance Algorithm Results
Chart: WCII
| All | 20% | 45% | 55% | 60% | 75%
WCII | 1 | 1.0272 | 1.0048 | 0.9737 | 0.9422 | 0.8404
Level | Miles | Trash Collected | Mild | Med | High
All | 91.64 | 1 | 0 | 0 | 0
20% | 87.45 | .98 | 0 | 0 | 0
45% | 77.37 | .85 | 0 | 0 | 0
55% | 70.71 | .75 | 19.8 | 3.2 | 0
60% | 69.00 | .71 | 21.2 | 15.2 | 3.6
75% | 60.86 | .58 | 27 | 19.6 | 55.4
Mild Inconvenience: 100-110% Full
Med Inconvenience: 110-120% Full
High Inconvenience: Over 120% Full
Notes: Omar

## Slide 23: Clarke-Wright Routes
Full Collection Week I
>45% Collection Week I
Weeks | Number of Stops | 
 | Full Collection | > 45% Collection
Week I | 501 | 292
Week II | 501 | 419
Week III | 501 | 326
Week IV | 501 | 422
Week V | 501 | 311
Total Points | 2,505 | 1770
Notes: Omar

## Slide 24: Routes Using Clarke-Wright (Full Case)
Notes: Omar

## Slide 25: Miles Travelled Using Clarke-Wright Algorithm
Chart: Distance Travelled (Miles)
| Week I | Week II | Week III | Week IV | Week V
Full Collection | 81.4902 | 81.4902 | 81.4902 | 81.4902 | 81.4902
>45% Collection | 61.1227 | 73.1352 | 63.7817 | 73.0603 | 63.1661
Total
407.45
334.25
17.96% Decrease in Miles Travelled Over 5 Weeks
Notes: Omar

## Slide 26: WCCI Metric Comparison Clarke-Wright
Chart: WCCI
| Week I | Week II | Week III | Week IV | Week V
Full Collection | 1 | 1 | 1 | 1 | 1
>45% Collection | 1.1475 | 1.0657 | 1.1136 | 1.0725 | 1.0967
Average
1
1.0991
9.91% avg increase in WCCI over 5 Weeks
Notes: Omar

## Slide 27: Conclusion
Notes: Emilio

## Slide 28: Potential Future Input Pipeline
New Route With Minimal Travel Distance
SVM Class
Current Fill Status
Future Fill Status
Deep Learning
Hidden Markov
Model
Route Algorithm
Notes: Emilio: Talk about how Omar found an article and was inspired, we want to look at big bicture and connect to optimization and operations research.

## Slide 29: Conclusion
Implications:
  Routing using known fill status can improve overall efficiency of system
  Future developments in fill detection must be complemented with appropriate strategies
Limitations:
  Assumption that every household generates a similar amount of trash each week
Future Work:
  Consider problem statemet where which houses trash is collected from is optional

## Slide 30: References
https://www.researchgate.net/publication/327298796_Waste_level_detection_and_HMM_based_collection_scheduling_of_multiple_bins
Rensselaer Polytechnic Institute, Department of Industrial and Systems Engineering
Lehigh University, VRP Solver

## Slide 31: Appendix I: Clarke Wright Savings Algorithm
  STEP 1: Calculate the savings s(i, j) = d(D, i) + d(D, j) - d(i, j) for every pair (i, j) of demand points.
  STEP 2: Rank the savings s(i, j) and list them in descending order of magnitude. This creates the "savings list." Process the savings list beginning with the topmost entry in the list (the largest s(i, j)).
  STEP 3: For the savings s(i, j) under consideration, include link (i, j) in a route if no route constraints will be violated through the inclusion of (i, j) in a route, and if:
    a. Either, neither i nor j have already been assigned to a route, in which case a new route is initiated including both i and j.
    b. Or, exactly one of the two points (i or j) has already been included in an existing route and that point is not interior to that route (a point is interior to a route if it is not adjacent to the dpoints), in which case the link (i, j) is added to that same route.
    c. Or, both i and j have already been included in two different existing routes and neither point is interior to its route, in which case the two routes are merged.
  STEP 4: If the savings list s(i, j) has not been exhausted, return to Step 3, processing the next entry in the list; otherwise, stop: the solution to the VRP consists of the routes created during Step 3. (Any points that have not been assigned to a route during Step 3 must each be served by a vehicle route that begins at the depot D visits the unassigned point and returns to D.)
Notes: Greg